## Slide 1: Home Inspection (驗屋)
Presented by Edward Tsang (曾慶樂)
(License # (牌照號碼): 80018)

## Slide 2: Code of Practice (業務守則)
Inspect readily accessible, visually observable, installed systems and components (目測易進入之已安裝的系統和設備);
Provide a written report stating (提供書面報告, 說明):
(i) Those not functioning, deficient, unsafe
or near end of services life (系統和設備的
故障, 損壞, 不安全或接近使用壽命期限);
(ii) Recommendations (建議);
(iii) Implications (可能引致之後果);
(iv) Limitations (限制)

## Slide 3: Scope of Inspection (驗屋範圍)
Roof (屋頂)
Exterior (外部)
Structural (結構)
Electrical (電氣)
Heating and Cooling (暖氣及空調)
Plumbing (水務)
Insulation (保温)
Interior (內部)

## Slide 4: Roof Systems (屋頂系統)
Roof Coverings (屋頂瓦面)
Roof Flashings (屋頂防水板)
Chimneys, Skylights and Roof Penetrations
(煙囪, 天窗及其他屋頂附件)
Roof Drainage Systems (屋頂排水系統)

## Slide 5: Roof Covering Defect Examples (瓦面損壞例子)
Near end of life (接近壽命期限)
Missing/Curling/Splitting (甩掉/捲曲/爆裂)
Cracking (裂開)
Alligatoring (龜裂)

## Slide 6: Roof Flashing Defect Examples (屋頂防水板損壞例子)
Not into mortar joints (未嵌入接合處)
Proper installation (正確安裝)
Proper installation (正確安裝)
No clearance (沒有两吋間隙)

## Slide 7: Chimney/Skylight/Penetration Defect Examples (煙囪/天窗/屋頂其他附件損壞例子)
Skylight sealant defective (天窗密封 膠損壞)
Skylight leaks (天窗漏水)
Chimney wall damaged (煙囪牆身損壞)
Exposed nail heads (釘頭外露)

## Slide 8: Roof Drainage System Defect Examples (屋頂排水系統損壞例子)
Vulnerable areas (易損壞之處)
Vulnerable areas (易損壞之處)
No Kickout flashings (缺少導引防水板裝置)
Discharge on roof (卸水流經屋頂)

## Slide 9: Exterior Systems (外部系統)
Exterior Wall (外牆)
Doors/Windows Exterior Side (門窗外部)
Decks/Balconies/Steps (露天平台/陽台/外部梯級)
Soffits/Fascias/Trims (屋簷/護板)
Lot Grading/Surface Drainage (地勢/排雨水系統)
Landscaping (樹木)
Driveways/Walks/Patio (車道/人行道/天井)
Retaining Wall (擋土牆)
Garage/Carport (車庫)

## Slide 10: Common Exterior defects (1) (常見外部系統毛病) (1)
Brick wall no weep hole (磚牆缺少淚孔)
Stucco wall crack (灰泥牆有裂痕)
Stucco wall moisture in (灰泥牆水氣滲入)
Too close to grade (牆身太接近地面)

## Slide 11: Common Exterior defects (2) (常見外部系統毛病) (2)
Door threshold too low (門檻太低)
Window caulking ineffective (窗框堵縫失效)
Damaged window well (窗井損壞)
Well wall damaged (窗井牆損壞)

## Slide 12: Common Exterior defects (3) (常見外部系統毛病) (3)
Deck post rot (平台支柱腐爛)
Deck support inadequate (平台支撑不足)
Soffit loose (屋簷底模鬆脫)
Fascia board rotted (封檐板腐爛)

## Slide 13: Common Exterior defects (4) (常見外部系統毛病) (4)
Old perimeter drain tile (陳舊外圍排水瓦通)
Discharge too close (排水離屋太近)
Walkway trip hazard (人行道有絆倒危險)
Railings ineffective (圍欄失效)

## Slide 14: Common Exterior System Defects (5) (常見外部系統毛病) (5)
Retailing wall leaning (擋土牆傾斜/爆裂)
Retaining wall rotted (擋土牆腐爛)
Garage gastight damaged (車房氣密削弱)
Mandoor not self-closing (人門不自動全關)

## Slide 15: Structural Systems (結構系統)
Foundation Structure (地基結構)
Floor Structure (地板結構)
Wall Structure (牆壁結構)
Ceiling Structure (天花結構)
Roof Structure (屋頂結構)

## Slide 16: Common Structural System Defects (常見結構系統毛病)
Vertical crack (垂直裂縫)
Horizontal crack (水平裂縫)
Prior repair (先前維修)
Cut truss (切斷屋頂椽子構架)

## Slide 17: Electrical Systems (電氣系統)
Service Lines (供電線路)
Service Entrance Conductors (供電導體)
Service Equipment/Main Disconnect (總開關)
Service Grounding (接地裝置)
Service Panel/Subpanel (供電掣箱)
Distribution Conductors (分配電力導體)
Over Current Protection (超載保護裝置)
Lightings/Switches/Receptacles (電掣/插座)
GFCI/AFCI (漏電/電弧斷流器)

## Slide 18: Common Electrical System defects (常見電氣系統毛病)
Single core aluminum wire (單枝鋁線)
Knob-and-Tube wiring (瓷珠瓷管佈線)
Unprotected opening (無保護的開口)
GFCI missing (無漏電保護器)

## Slide 19: Heating Systems (供暖系統)
Fuel Storage Systems (燃料儲存系統)
Fuel Distribution Systems (燃料分發系統)
Installed Heating Equipment (加熱設備)
Vent Systems/Chimneys (排氣系統/煙囪)
Ductworks and Registers (風槽/風咀)
Radiators/Convectors/Piping (散熱器/管道)
Controls (控制裝置)
Heat Recovery Ventilators (換熱通風機)

## Slide 20: Common Heating System Defects (常見供暖系統毛病)
Buried oil tank (地下油缸)
Old/rusty furnace (陳舊/生銹火爐)
Zone valve inoperative (區域閥損壞)
Outlet above electric heater (插座位於電爐上)

## Slide 21: Cooling Systems (空調系統)
Air Conditioning System (空調系統)
Heat Pump (熱泵系統)
Outdoor Unit (室外部件)
Indoor Unit (室內部件)
Refrigerant Lines (製冷劑管道)
Ducts and Registers (風槽/風咀)

## Slide 22: Common Cooling System Defects (常見空調系統毛病)
Old air-conditioning unit (陳舊空調機)
Insulation missing (液體喉缺少保温)
Dryer exhaust too close (乾衣機排氣口太近)
Condensate drain blocked (冷凝排水淤塞)

## Slide 23: Plumbing Systems (水務系統)
Water Supply/Distribution Systems
(供水/配水系統)
Fixtures and Faucets (水務裝置及喉具)
Drain, Waste & Vent Systems (排污系統)
Water Heating Equipment (熱水爐)
Pumps (水泵)
Exhaust Fans (抽氣扇)

## Slide 24: Common Plumbing System Defects (常見水務系統毛病)
Polybutylene (Poly-B) piping (聚丁烯喉管)
Old copper piping (陳舊銅喉管)
Old water heater (陳舊熱水器)
Bathtub tile loose (浴缸瓷磚鬆脫)

## Slide 25: Insulation Systems (保温系統)
Attic/Flat Roof Insulation (閣樓/平屋頂保温)
Attic Ventilation (閣樓通風)
Air/Vapour Barrier (空氣/水蒸氣阻隔層)
Wall Insulation (外牆保温)
Floor Insulation (above unheated area)
(地板保温 (位於無暖氣地方之上方)
Crawlspace Ventilation (矮土庫通風)

## Slide 26: Common Insulation Defects (常見保温毛病)
Vermiculite insulation (蛭石保温)
Inadequate insulation (保温不足夠)
Insulation voids and gaps (保温空隙)
Attic mold (閣樓發霉)

## Slide 27: Interior Systems (內部系統)
Ceilings/Walls/Floors (天花/牆壁/地板)
Steps/Stairways/Railings (梯級/樓梯/圍欄)
Countertops/Cabinets (檯面/牆櫃)
Doors/Windows (門/窗)
Fireplace/Wood Stove (壁爐/火爐)
Basement (土庫)
Crawlspace (矮土庫)

## Slide 28: Common Interior System Defects (常見內部系統毛病)
Ceiling stains (天花水漬)
Wall water damage (牆身損害)
Stairs handrail missing (樓梯沒有扶手)
Window lost seal (窗門密封失效)

## Slide 29: Enjoy Your Home
安 享 家 樂